## Slide 1
Workplace Hazardous Materials Information System (WHMIS)

## Slide 2: What is WHMIS?

## Slide 3: WHMIS
WHMIS was designed to address employers’ and workers’ right to know about the hazards and safe work practices related to certain chemicals and infectious biological substances. Materials that are subject to WHMIS legislation is called controlled products
Requires employees to use products safely
Requires the employer to ensure that employees are trained to use products safely and have access to information on safe use

## Slide 4: Key Elements to WHMIS
Identification : Labeling/Hazard Symbols
Knowledge: Worker Education & Training
Information: Material Safety Data Sheets

## Slide 5: WHMIS Responsibilities
Suppliers
  Determining which products are “controlled” products and classifying appropriately
  Establishing health and safety information regarding a product
  Labelling products with WHMIS labels
  Preparing and providing MSDS’s for customers and updating them
Employers
  Ensure all controlled products at the work sites have WHMIS labels
  Make MSDSs available and accessible to workers
  Train workers to read labels and MSDS’s, recognize WHMIS labels, how to handle, use and store controlled products and, if required, use personal protective equipment
Employees
  Participate in education and training provided by the employer
  Follow prescribed safe work procedures

## Slide 6: What is a Controlled Product?
Controlled products are materials, products, or substances that meet any of the criteria for one or more of the six WHMIS Hazard Classes as defined in the Federal Controlled Product Regulation
Exclusions
The following are exempt from the suppliers responsibilities of WHMIS (no label or MSDS required):
  Consumer retricted products
  Explosives
  Cosmetics, drug, food, or devices
  Pesticides, herbicides, and insecticides
  Radioactive material

## Slide 7: WHMIS Hazard Symbols
These hazard symbols on the label identify the product as controlled by WHMIS and classify the type of hazard.
CLASS A Compressed Gas
CLASS B Flammable and Combustible Material
CLASS C Oxidizing Materials
CLASS D-1 Poisonous and Infectious Material (material causing immediate and serious effects)
CLASS D-2 Poisonous and Infectious Material (material causing other toxic effects)
CLASS D-3 Poisonous and Infectious Material (Biohazardous Infectious Material)
CLASS E Corrosive Material
CLASS F Dangerously Reactive Material

## Slide 8: Class A: Compressed Gas
Characteristics
  Gas inside cylinder is under pressure
Hazards
  Cylinder may explode if dropped or heated
  Hazards associated with force of explosion and contents of cylinder
Handling and Use
  Transport with specialized cart
  Use gas specific regulator
  Store away from heat and fire sources
  Test connections for leaks
  Ensure cylinders are properly secured
Notes: Any material that is normally a gas which is placed under pressure or chilled, and contained by a cylinder is considered to be a compressed gas. These materials are dangerous because they are under pressure. If the cylinder is broken, the container can 'rocket' or 'torpedo' at great speeds and this is a danger to anyone standing too close. If the cylinder is heated (by fire or rise in temperature), the gas may try to expand and the cylinder will explode. Leaking cylinders are also a danger because the gas that comes out is very cold and it may cause frostbite if it touches your skin (for example: carbon dioxide or propane). Common examples include: compressed air, carbon dioxide, propane, oxygen, ethylene oxide, and welding gases. The hazard symbol is a picture of a cylinder or container of compressed gas surrounded by a circle.
Additional dangers may be present if the gas has other hazardous properties. For example: propane is both a compressed gas and it will burn easily. Propane would have two hazard symbols - the one for a compressed gas and another to show that it is a flammable material.

## Slide 9: Class B: Flammable and Combustible
Characteristics
  May burn or explode when exposed to heat, sparks, or flames
Hazards
  May ignite spontaneously
  May ignite upon decomposing or being exposed to water
Handling and Use
  Store away from Class C: Oxidizing Materials
  Avoid storing near sources of heat, sparks, or flames
  Keep containers tightly sealed
  Ground and bond when dispensing from 25 L containers
  Store in flammable cabinets if quantities exceed 50 L
  Transport using secondary containment
Notes: Flammable means that the material will burn or catch on fire easily at normal temperatures (below 37.8 degrees C or 100 deg F). Combustible materials must usually be heated before they will catch on fire at temperatures above normal (between 37.8 and 93.3 deg C or 100 and 200 deg F). Reactive flammable materials are those which may suddenly start burning when it touches air or water, or may react with air or water to make a flammable gas. The material may be a solid, liquid or gas which makes up the different divisions that fall under this class. Common examples include: propane, butane, acetylene, ethanol, acetone, turpentine, toluene, kerosene, Stoddard solvent, spray paints and varnish. The symbol for this class is a flame with a line under it inside a circle.

## Slide 10: Class C: Oxidizing Material
Characteristics
  Can promote burning or explosions of other materials by providing an oxygen source for combustion
Hazards
  May burn skin and eyes on contact
  Increase fire and explosion hazard
  May cause combustibles to explode or react violently
Handling and Use
  Transport and store separately from flammables and organics
  Store in non-corroding containers
  Store away from sources of heat and ignition
  Wear proper personal protective equipment
Examples
  Hydrogen peroxide
  Bleach
  Nitrates
Notes: Oxygen is necessary for a fire to occur. Some chemicals can cause other materials to burn by supplying oxygen. Oxidizers do not usually burn themselves but they will either help the fire by providing more oxygen or they may cause materials that normally do not burn to suddenly catch on fire (spontaneous combustion). In some cases, a spark or flame (source of ignition) is not necessary for the material to catch on fire but only the presence of an oxidizer. Oxidizers can also be in the form of gases (oxygen, ozone), liquids (nitric acid, perchloric acid solutions) and solids (potassium permanganate, sodium chlorite). Some oxidizers such as the organic peroxide family are extremely hazardous because they will burn (they are combustible) as well as they have the ability to provide oxygen for the fire. They can have strong reactions which can result in an explosion. The symbol for oxidizing materials is an "o" with flames on top of it inside a circle.

## Slide 11: Class D-1: Poisonous and Infectious
Division 1: Materials causing immediate and serious toxic effects (acute)
  Subdivision A: Very toxic material
  Subdivision B: Toxic material
Characteristics
  Poisonous and potentially fatal materials resulting in immediate and severe harm
Hazards
  Small quantities may be harmful or lethal
  May cause immediate death or serious harm if inhaled, swallowed, or absorbed through the skin
Handling and Use
  Avoid skin and eye contact
  Minimize vapor exposure
  Wear the recommended personal protective equipment
  Wash hands after handling
Examples
  Cyanides
  All halogens
Notes: Class D materials are those which can cause harm to your body. They are divided into three major divisions.
Division 1: Materials Causing Immediate and Serious Toxic Effects
These are materials that are very poisonous and immediately dangerous to life and health. Serious health effects such as burns, loss of consciousness, coma or death within just minutes or hours after exposure are grouped in this category. Most D-1 materials will also cause longer term effects as well (those effects that are not noticed for months or years). Examples of some D-1 materials include carbon monoxide, sodium cyanide, sulphuric acid, toluene-2,4-diisocyanate (TDI), and acrylonitrile. The symbol for Class D - Division 1 (D-1) is a skull and crossed bones inside a circle.
Division 2: Materials Causing Other Toxic Effects
These materials are poisonous as well. Their effects are not always quick, or if the effects are immediate but they are only temporary. The materials that do not have immediate effects, however, may still have very serious consequences such as cancer, allergies, reproductive problems or harm to the baby, changes to your genes, or irritation / sensitization which have resulted from small exposures over a long period of time (chronic effects).
Division 2 of Class D has two subclasses called D2A (very toxic) and D2B (toxic). While it is not a legal requirement for the WHMIS sub-classification to be reported on the Material Safety Data Sheet (MSDS) nor is it a requirement for classes D2A or D2B to be distinguished on the label, it is often possible to make this distinction using the health hazard information on the label and/or the MSDS.
Products are typically classified as D2A (very toxic) if the chemical has been shown to be carcinogenic, embryo toxic, teratogenic, mutagenic (to reproductive cells), reproductive toxic, sensitizer (to respiratory tract) or chronic (long-term) toxicity (at low doses). Subdivision D2B (toxic) covers mutagenic (to non-reproductive cells), sensitization of the skin, skin or eye irritation, as well as chronic toxic effects.
Examples include: asbestos fibres, mercury, acetone, benzene, quartz silica (crystalline), lead and cadmium. The symbol for materials causing other toxic effects looks like a "T" with an exclamation point "!" at the bottom inside a circle.
Division 3: Biohazardous Infectious Materials
These materials are organisms or the toxins they produce that can cause diseases in people or animals. Included in this division are bacteria, viruses, fungi and parasites. As these organisms can live in body tissues and fluids, they should be treated as toxic. Urine and feces should be treated as toxic only if they are visibly contaminated with blood. Biohazardous infectious materials are usually found in a hospital, health care facility, laboratories, veterinary practices and research facilities. Workers in these places do not usually know which tissues or fluids contain dangerous organisms. For this reason, the workers assume that every sample is dangerous and proper protection is used all the time. Examples of biohazardous infectious materials include the AIDS/HIV virus, Hepatitis B and salmonella. The symbol for this division looks like three "c"s joined together with a little circle in the middle all inside a circle.

## Slide 12: Class D-2: Poisonous and Infectious
Division 2: Materials causing other toxic effects (chronic, delayed)
  Subdivision A: Very toxic material
  Subdivision B: Toxic material
Characteristics
  Materials which have harmful effects after repeated exposures over long periods of time
Hazards
  May cause death or permanent injury
  May cause organ damage, cancer, birth defects, or sterility
  May lead to sensitization or allergies
Handling and Use
  Avoid skin and eye contact
  Minimize vapor exposure
  Wear the recommended personal protective equipment
  Wash hands after handling
Examples
  Asbestos
  Benzene
Notes: Class D materials are those which can cause harm to your body. They are divided into three major divisions.
Division 1: Materials Causing Immediate and Serious Toxic Effects
These are materials that are very poisonous and immediately dangerous to life and health. Serious health effects such as burns, loss of consciousness, coma or death within just minutes or hours after exposure are grouped in this category. Most D-1 materials will also cause longer term effects as well (those effects that are not noticed for months or years). Examples of some D-1 materials include carbon monoxide, sodium cyanide, sulphuric acid, toluene-2,4-diisocyanate (TDI), and acrylonitrile. The symbol for Class D - Division 1 (D-1) is a skull and crossed bones inside a circle.
Division 2: Materials Causing Other Toxic Effects
These materials are poisonous as well. Their effects are not always quick, or if the effects are immediate but they are only temporary. The materials that do not have immediate effects, however, may still have very serious consequences such as cancer, allergies, reproductive problems or harm to the baby, changes to your genes, or irritation / sensitization which have resulted from small exposures over a long period of time (chronic effects).
Division 2 of Class D has two subclasses called D2A (very toxic) and D2B (toxic). While it is not a legal requirement for the WHMIS sub-classification to be reported on the Material Safety Data Sheet (MSDS) nor is it a requirement for classes D2A or D2B to be distinguished on the label, it is often possible to make this distinction using the health hazard information on the label and/or the MSDS.
Products are typically classified as D2A (very toxic) if the chemical has been shown to be carcinogenic, embryo toxic, teratogenic, mutagenic (to reproductive cells), reproductive toxic, sensitizer (to respiratory tract) or chronic (long-term) toxicity (at low doses). Subdivision D2B (toxic) covers mutagenic (to non-reproductive cells), sensitization of the skin, skin or eye irritation, as well as chronic toxic effects.
Examples include: asbestos fibres, mercury, acetone, benzene, quartz silica (crystalline), lead and cadmium. The symbol for materials causing other toxic effects looks like a "T" with an exclamation point "!" at the bottom inside a circle.
Division 3: Biohazardous Infectious Materials
These materials are organisms or the toxins they produce that can cause diseases in people or animals. Included in this division are bacteria, viruses, fungi and parasites. As these organisms can live in body tissues and fluids, they should be treated as toxic. Urine and feces should be treated as toxic only if they are visibly contaminated with blood. Biohazardous infectious materials are usually found in a hospital, health care facility, laboratories, veterinary practices and research facilities. Workers in these places do not usually know which tissues or fluids contain dangerous organisms. For this reason, the workers assume that every sample is dangerous and proper protection is used all the time. Examples of biohazardous infectious materials include the AIDS/HIV virus, Hepatitis B and salmonella. The symbol for this division looks like three "c"s joined together with a little circle in the middle all inside a circle.

## Slide 13: Class D-3: Poisonous and Infectious
Division 3: Biohazardous infectious material
Characteristics
  Infectious agents or biological toxins resulting in serious disease or death
Hazards
  May cause serious disease resulting in illness or death
Handling and Use
  Work with materials in designated area (ie. Biosafety cabinet)
  Disinfect area after cleaning
  Wash hands after handling
  Wear proper personal protective equipment
Examples
  E. Coli
  Tissues
  Viruses
Notes: Class D materials are those which can cause harm to your body. They are divided into three major divisions.
Division 1: Materials Causing Immediate and Serious Toxic Effects
These are materials that are very poisonous and immediately dangerous to life and health. Serious health effects such as burns, loss of consciousness, coma or death within just minutes or hours after exposure are grouped in this category. Most D-1 materials will also cause longer term effects as well (those effects that are not noticed for months or years). Examples of some D-1 materials include carbon monoxide, sodium cyanide, sulphuric acid, toluene-2,4-diisocyanate (TDI), and acrylonitrile. The symbol for Class D - Division 1 (D-1) is a skull and crossed bones inside a circle.
Division 2: Materials Causing Other Toxic Effects
These materials are poisonous as well. Their effects are not always quick, or if the effects are immediate but they are only temporary. The materials that do not have immediate effects, however, may still have very serious consequences such as cancer, allergies, reproductive problems or harm to the baby, changes to your genes, or irritation / sensitization which have resulted from small exposures over a long period of time (chronic effects).
Division 2 of Class D has two subclasses called D2A (very toxic) and D2B (toxic). While it is not a legal requirement for the WHMIS sub-classification to be reported on the Material Safety Data Sheet (MSDS) nor is it a requirement for classes D2A or D2B to be distinguished on the label, it is often possible to make this distinction using the health hazard information on the label and/or the MSDS.
Products are typically classified as D2A (very toxic) if the chemical has been shown to be carcinogenic, embryo toxic, teratogenic, mutagenic (to reproductive cells), reproductive toxic, sensitizer (to respiratory tract) or chronic (long-term) toxicity (at low doses). Subdivision D2B (toxic) covers mutagenic (to non-reproductive cells), sensitization of the skin, skin or eye irritation, as well as chronic toxic effects.
Examples include: asbestos fibres, mercury, acetone, benzene, quartz silica (crystalline), lead and cadmium. The symbol for materials causing other toxic effects looks like a "T" with an exclamation point "!" at the bottom inside a circle.
Division 3: Biohazardous Infectious Materials
These materials are organisms or the toxins they produce that can cause diseases in people or animals. Included in this division are bacteria, viruses, fungi and parasites. As these organisms can live in body tissues and fluids, they should be treated as toxic. Urine and feces should be treated as toxic only if they are visibly contaminated with blood. Biohazardous infectious materials are usually found in a hospital, health care facility, laboratories, veterinary practices and research facilities. Workers in these places do not usually know which tissues or fluids contain dangerous organisms. For this reason, the workers assume that every sample is dangerous and proper protection is used all the time. Examples of biohazardous infectious materials include the AIDS/HIV virus, Hepatitis B and salmonella. The symbol for this division looks like three "c"s joined together with a little circle in the middle all inside a circle.

## Slide 14: Class E: Corrosive Material
Characteristics
  Materials that will erode metals or destroy tissues
Hazards
  Will burn human tissue upon contact
  Can corrode laboratory materials, in particular metals
Handling and Use
  Store acids and bases separately
  Store chemicals in non-corroding containers
  When possible, work in a fume hood
  Wear recommended personal protective equipment
Examples
  Strong acids and bases
  Hydrogen Fluoride
Notes: Class D materials are those which can cause harm to your body. They are divided into three major divisions.
Division 1: Materials Causing Immediate and Serious Toxic Effects
Corrosive is the name given to materials that can cause severe burns to skin and other human tissues such as the eye or lung, and can attack clothes and other materials including metal. Corrosives are grouped in this special class because their effects are permanent (irritants whose effects may be similar but temporary are grouped in Class D-2). Common corrosives include acids such as sulphuric and nitric acids, bases such as ammonium hydroxide and caustic soda and other materials such as ammonia, chlorine, and nitrogen dioxide. The symbol for a corrosive is a picture of two test tubes pouring liquid on a bar (piece of metal) and a hand with lines coming off of them inside a circle.

## Slide 15: Class F: Dangerously Reactive
Characteristics
  Materials may undergo unexpected reactions under certain conditions
Hazards
  May be chemically unstable
  May vigorously polymerize
  May react with water to release a toxic or flammable gas
  May explode if exposed to heat or shock
  May burn unexpectedly
Handling and Use
  Follow MSDS recommendations for storage and use
  Wear recommended personal protective equipment
  Examine storage containers frequently
  Store and transport securely
Examples
  Azides
  Hydrazine
  Ether
Notes: A material is considered to be dangerously reactive if it shows three different properties or abilities: first, if it can react very strongly and quickly (called "vigorously") with water to make a toxic gas; second, if it will react with itself when it gets shocked (bumped or dropped) or if the temperature or pressure increases; and thirdly, if it can vigorously join to itself (polymerization), break down (decomposition) or lose extra water such that it is a more dense material (condensation). If a material is dangerously reactive, it will most likely be described as "unstable". Most of these materials can be extremely hazardous if they are not handled properly because they can react in such a quick manner very easily. Examples of these products are ethyl acrylate, vinyl chloride, ethylene oxide, picric acid and anhydrous aluminum chloride. The symbol for dangerously reactive materials is a picture of a test tube with sparks or lines coming out of the tube surrounded by a letter "R" inside a circle.

## Slide 16: Identification: Labels/Hazard Symbols
Labels are the first identification to the user that a substance is a WHMIS controlled product.
Labels must be:
  Visible in normal conditions of storage
  Easy to see
  Durable
  Attached in such a manner that they will remain in good condition
The three types of labels in the WHMIS system are:
  Supplier Label
  Workplace Label
  Other means of identification

## Slide 17: Supplier Labels
Must be attached by the supplier when the material arrives at the workplace to identify shipments that include controlled products
Supplier labels must contain:
  Product Identifier
  Suppliers Identifier
  Hazard Symbols
  Risk Phrases
  Precautionary Measures
  First Aid Measures
  MSDS Reference

## Slide 18: Workplace Labels
Workplace labels must be used when:
  A controlled product is delivered to the workplace in bulk and a supplier label is not available
  A controlled product is transferred to a smaller portable container for use in the workplace
  The supplier label on the container becomes unreadable, damaged, or detached, and a replacement supplier label is not available
Workplace labels need to show:
  The product identifier
  Safe handling procedures
  Reference to an MSDS

## Slide 19: What is MSDS?
MSDS is an acronym for: Material Safety Data Sheet
Material Safety Data Sheet must be obtained at the time of purchase
A MSDS must be less than 3 years old
MSDS's must be available for use and reference at all times
MSDS provides information on:
  health effects of overexposure
  health evaluation related to product handling, storage and use
  measures to protect workers at risk of overexposure
  emergency procedures

## Slide 20: MSDS
The MSDS must contain the following sections and information:
  Section 1: Product identification and use
  Section 2: Hazardous ingredients
  Section 3: Physical data
  Section 4: Fire and explosive data
  Section 5: Reactivity data
  Section 6: Toxicology properties
  Section 7: Preventative measure
  Section 8: First Aid measures
  Section 9: Preparation date

## Slide 21: MSDS FETCH
West Vancouver School District utilize the computerized WHMIS system known as MSDS FETCH
MSDS FETCH contains over 10,000 MSDS that can be accessed in a few minutes by phone, fax and online
How to access MSDS FETCH
  It is available to members 24 hours a day, 7 days a week
  Website: http://msdsfetch.vsb.bc.ca
    Login: sd45westvan
    Password: 6047313492
  Call 604-713-5273 office hours M-F 8:30am to 4:30pm

## Slide 22: WHMIS 2015
In February 2015, Canada amended the Hazardous Products Act and published the Hazardous Products Regulations in order to incorporate the GHS into WHMIS
To allow time for suppliers, employers and workers to adjust, implementation will take place over a multi-year transition period where both WHMIS (WHMIS 1988) and WHMIS 2015 may be used in the workplace

## Slide 23: WHMIS 2015 – What are the Changes?
WHMIS has aligned with the Globally Harmonized System of Classification and Labelling of Chemicals (GHS) and the goal is to have a common set of rules used worldwide
Aligning WHMIS with GHS helps to:
  Enhance the protection of worker health and safety by having improved and consistent hazard information
  Encourage safe transport, handling, and use of hazardous products
  Promote better emergency response
  Promote regulatory efficiency and compliance
  Facilitate international trade
  GHS will not replace WHMIS, however, will create some important changes to WHMIS
New classification rules and hazard classes
A standardized format for Safety Data Sheets (formerly MSDS)
New hazard pictograms
New label requirements

## Slide 24: Hazard Group
WHMIS 2015 applies to two major groups of hazards: physical, and health. Each hazard group includes hazard classes that have specific hazardous properties.
  Physical hazards group: based on the physical or chemical properties of the product - such as flammability, reactivity, or corrosivity to metals
  Health hazards group: based on the ability of the product to cause a health effect - such as eye irritation, respiratory sensitization (may cause allergy or asthma symptoms or breathing difficulties if inhaled), or carcinogenicity (may cause cancer)

## Slide 25: Hazard Class and Category
Hazard classes are a way of grouping together products that have similar properties. Most of the hazard classes are common to GHS and will be used worldwide by all countries that have adopted GHS. Some hazard classes are specific to WHMIS 2015
Each hazard class contains at least one category. The hazard categories are assigned a number (e.g., 1, 2, etc.) Categories may also be called "types". Types are assigned an alphabetical letter (e.g., A, B, etc.). In a few cases, sub-categories are also specified. Subcategories are identified with a number and a letter (e.g., 1A and 1B)
Some hazard classes have only one category (e.g., corrosive to metals), others may have two categories (e.g., carcinogenicity (cancer)) or three categories (e.g., oxidizing liquids). There are a few hazard classes with five or more categories (e.g., organic peroxides)
The category tells you about how hazardous the product is (that is, the severity of hazard)
Category 1 is always the greatest level of hazard. If Category 1 is further divided, Category 1A within the same hazard class is a greater hazard than category 1B
Notes: Each hazard class contains at least one category. The hazard categories are assigned a number (e.g., 1, 2, etc.) Categories may also be called "types". Types are assigned an alphabetical letter (e.g., A, B, etc.). In a few cases, sub-categories are also specified. Subcategories are identified with a number and a letter (e.g., 1A and 1B).
Some hazard classes have only one category (e.g., corrosive to metals), others may have two categories (e.g., carcinogenicity (cancer)) or three categories (e.g., oxidizing liquids). There are a few hazard classes with five or more categories (e.g., organic peroxides).
The category tells you about how hazardous the product is (that is, the severity of hazard).
Category 1 is always the greatest level of hazard (that is, it is the most hazardous within that class). If Category 1 is further divided, Category 1A within the same hazard class is a greater hazard than category 1B.
Category 2 within the same hazard class is more hazardous than category 3, and so on.
There are a few exceptions to this rule. For example, for the Gases under pressure hazard class, the hazard categories are "Compressed gas", "Liquefied gas", "Refrigerated liquefied gas" and "Dissolved gas". These classes relate to the physical state of the gas when packaged and do not describe the degree of hazard.
In addition, the Reproductive Toxicity hazard class has a separate category called "Effects on or via lactation". "Effects on or via lactation" was not assigned a specific numbered category. Reproductive toxicity also has Categories 1 and 2 which relate to effects on fertility and/or the unborn child. Effects on or via lactation is considered a different, but related hazard within the Reproductive toxicity class.

## Slide 26: GHS Pictograms
 | Carcinogenicity Respiratory sensitization Reproductive toxicity Specific target organ toxicity – repeated exposure Specific target organ toxicity – single exposure (category 1, 2) Aspiration hazard Germ cell mutagenicity
 | Corrosive to metals Serious eye damage Skin corrosion
 | Gases under pressure
 | Biohazardous infectious material
 | Hazardous to the aquatic environment Canada will not be implementing
 | Flammables (gases, aerosols, liquids, solids) Self-reactive substances and mixtures Pyrophoric liquids, solids, and gases Self-heating substances and mixtures Substances and mixtures that in contact with water emit flammable gas Organic peroxides
 | Skin sensitization Acute toxicity (harmful) Specific target organ toxicity – single exposure (category 3) Eye irritation Skin irritation Hazardous to the ozone layer
 | Acute toxicity (severe)
 | Oxidizing gases, liquids, solids
 | Self-reactive substances and mixtures Organic peroxides Explosives

## Slide 27: Safety Data Sheets (SDS)
Updated terminology for the MSDS
Will consist of 16 sections and variable number of pages
Will not need to be updated every 3 years
Must be current at time of sale/import
Section | Hazardous Product Regulations Heading
1 | Identification
2 | Hazard identification (including classification and label text)
3 | Composition/information on ingredients
4 | First-aid measures
5 | Fire-fighting measures
6 | Accidental release measures
7 | Handling and storage
8 | Exposure controls/personal protection
9 | Physical and chemical properties
10 | Stability and reactivity
11 | Toxicological information
12-15 | Ecological, transport and regulatory information, disposal considerations
16 | Other information

## Slide 28: Safety Data Sheets (SDS)
Remember the four basic questions that the SDS should answer
  Identify of the product and supplier?
  Hazards of the product?
  Precautions you should take?
  What to do in an emergency?
Click here for an example
  Safety Data Sheets

## Slide 29: Labels
Suppliers Labels will require the following:
  The pictogram, signal word, and hazard statement are to be grouped together
  To be clearly and prominently displayed on the container
  To be easy to read, and
  To be in contrast with other information on the product or container
Workplace Labels will require the following:
  Product name
  Safe handling precautions, may include pictogram or other supplier label information
  Reference to the SDS (if available)
An example of a supplier’s label

## Slide 30: Label Requirements – Comparison

## Slide 31
Questions?
Contact Human Resources at 604-981-1000
or visit us at the School Board Office